## Slide 1
Chest Percussion and Cough Assist

## Slide 2
Learning Objectives
At the end of this session participants should:
Have basic knowledge of what chest percussion is
Why it might be required by the CYPs using the service
Understand how to perform chest percussion
Understand what a cough assist machine is
Why cough assist is used as a treatment
How to use a cough assist
Understand and discuss the precautions and contraindications of these therapies

## Slide 3
What is Chest Percussion?
Chest percussion involves “patting” over the lungs of a CYP to loosen thick secretions/mucus on the lungs to be coughed out
The CYP will have a prescription for chest percussions which will usually state how long and where to “pat” them. An example might be “10 minutes patting on right and left side”
It should be clear in the CYPs care plan what time of the day they are to have their chest percussion to fit around their routine
Chest percussion can also be done as a PRN therapy for those who are prescribed it. This can help CYPs who might be acutely unwell with respiratory problems

## Slide 4
Why do we do Chest Percussions?
Conditions which cause an excessive build up of mucus/secretions including COPD and Cystic fibrosis
For CYPs prone to chest infections – chest percussion can reduce the risk of hospital admissions
CYPs with degenerative muscle weaknesses, who struggle to build enough effort to cough, may benefit from chest percussion
Chest percussion is sometimes done as part of a routine with nebulisers to loosen up the thick secretions and also before ‘cough assist’ which may encourage expectoration

## Slide 5
Before performing Chest Percussions
We must ensure:
The CYP has chest percussion documented in their Care Plan
It is NOT appropriate to do chest percussion on a CYP who does not receive this therapy as part of their treatment plan
Follow the instructions on the care plan RE: time, position and duration of treatment
Explain to the CYP and gain consent for the procedure

## Slide 6
How to perform Chest Percussions
Position the CYP according to the instruction in their Care Plan – there are 4 common positions
Laid on left side- percussion over right lung
Laid on back- front upper lung lobes
Laid on Back- Back of the lung
Laid on right side- percussion over left lung

## Slide 7
How to perform Chest Percussions
Fold a towel in half and place over the area you are going to ‘pat’. The rationale for the use of the towel is to cushion the area
Chest percussion should NEVER be performed on bare skin
The ‘pat’ is performed using a cupped hand and a soft wrist
The ‘pat’ needs to be appropriately firm to move the secretions effectively. It should be a fairly loud, hollow sound
Be careful not to pat over the spine, sternum or stomach
Monitor the CYP for any respiratory changes regularly during percussion
Remove any secretions with suctioning or a wipe
Move your hand from your wrist like the picture

## Slide 8
How to perform Chest Percussions

## Slide 9
Contraindications for Chest Percussion
Contraindications:
Rib Fractures
Osteoporosis (Weakened bones)
Osteogenesis imperfecta (Brittle bones)
Haemoptysis (Coughing up blood)
Head/Neck injuries
Vertebrae Fractures (A break to one of the bones in the spine)

## Slide 10
Precautions for Chest Percussion
Precautions
Timing of feeds – should be done before feeds or at least 45 minutes after
Timing of relevant meds – can be more effective to provide this treatment following mucus loosening medications such as saline nebulisers.
Be aware of any medical devices/lines in the area you are going to pat e.g. Hickman lines, portacaths. DO NOT percuss directly over these device/lines.

## Slide 11
What is Cough Assist?
Cough assist is a machine which facilitates the clearance of mucus in the lungs by encouraging a cough
This is achieved by blowing air (positive pressure) into the lungs, then pulling the air out (negative pressure) this mimics a cough
Cough assist is prescribed by a physiotherapist as a part of a CYPs treatment plan
A cough assist is NOT to be used on any CYP if not prescribed
The machine will be set to prescribed pressures depending on the ability of each CYP and how much support is needed

## Slide 12
What is Cough Assist?
The CYP may have several pre-set programmes programmed into the machine depending on the needs of the CYP
Some might have a setting for day to day use and a setting for when they are unwell
There can also be a pre-set of inhalation (positive) breaths only which don’t encourage a cough but help to inflate the CYPs lungs following cough assist treatment
You can use a cough assist with a facemask, catheter mount or a mouthpiece

## Slide 13
How does Cough Assist work?
Cough assist treatment consists of a prescribed number of “sequences”
A sequence consists of a number of ‘breath cycles’
These are a positive breath in, a negative breath out and a pause
E.G.
  ‘5 breaths per cycle for 4 sequences ’
  Which equals 4 LOTS OF 5 breaths
You should allow the CYP to rest for approx. 30 seconds between each sequence.
Most cycles end with an inhalation breath to give the CYP nice full lungs following the treatment.

## Slide 14
Why do our CYP need a Cough Assist?
The CYPs who may require using a cough assist machine are those with:
Diseases/disorders causing muscle weakness resulting in a weak cough e.g. Duchenne Muscular Dystrophy or Spinal Muscular Atrophy
Low muscle tone – where the CYP cannot build the effort to cough
Injuries that have caused paralysis – where signals from the brain are unable to reach the structures in the body that trigger a cough
Reasons why CYPs might benefit from cough assist:
If they have frequent lung infections e.g. pneumonia
They have frequent suctioning

## Slide 15
The Set-Up

## Slide 16
Fitting the Mask

## Slide 17
How to use a Cough Assist machine
Most Cough Assist machines that we see at Derian are simple to use. They have built in settings so you can press a button and the machine will carry out the therapy
Check the prescription for which pre-set is required and if necessary, change to this setting
Check the pressure/times are correct on the machine against the prescription for this setting
Hold the mask firmly against the CYP’s face or attach catheter mount
Press ‘start’ or ‘therapy’ to start the treatment
The machine will start to deliver the required programme

## Slide 18
How to use a Cough Assist machine

## Slide 19
How to use a Cough Assist machine
In between sequences you must remove the circuit from the CYP to allow them to get their breathe back
You may need to suction at this stage
Repeat according to prescription
Clean mask and interface with hot soapy water when finished
Ensure all attachments are packed away and the machine is on charge

## Slide 20
How it works – Treatment

## Slide 21
How it works – Treatment

## Slide 22
Cough Assist – Tracheostomy

## Slide 23
Cough Assist – Tracheostomy

## Slide 24
How to use the Cough Assist (Manual Switch)
There may be occasions when we get a CYP on a Cough Assist machine which requires the “manual switch” option
You will follow almost the exact same instructions as previously discussed
However, instead of pressing the therapy button on the machine to begin the treatment, you will use the manual switch
Some machines also have a remote with this manual switch on.

## Slide 25
How to use the Cough Assist (Manual Switch)
Shift the manual switch to the “+” side and hold to deliver the positive breath until the pressure is reached on the screen
Then shift the switch to the “-” side to begin the exhalation pull until the desired pressure is reached on the machine
Put the switch back to the neutral position to start the pause for the required time
Then repeat the amount of breath cycles to complete one sequence
You can then allow the CYP a rest for at least 30 seconds between each sequence before completing the prescribed amount.

## Slide 26
Contraindications of the Cough Assist
Contraindications:
Vomiting
Raised Intracranial Pressure (ICP)
Pneumothorax (air trapped between the chest wall and lung)
Facial fractures

## Slide 27
Precautions of the Cough Assist
Precautions
Patient Compliance – We should give time and encourage using the cough assist
Airway obstruction
Medication/Feed timings – Cough assist can be done before a feed but at least 45 minutes after
Cough assist can be more effective following chest percussion or mucus loosening nebulisers